## Slide 1: Efficient Robot Fabrication
Gary Pierson- Coach 1764
Chase Hill- COO 1764

## Slide 2: Course Overview
Material Basics
COTS (Components off the shelf)
Suppliers
Efficient shaping/machining

## Slide 3: Types of materials
Sheet materials
  Metals
  Plastics
Extrusions
  80/20
  Bosch

## Slide 4: Types of materials (Cont.)
Shaft Materials
  Hot Pressed
  Cold Pressed
  Drill Rod

## Slide 5: Suppliers
High-tech Automation

## Slide 6: Suppliers (Cont.)
McMaster Carr

## Slide 7: Suppliers (Cont.)
Skarda

## Slide 8: Suppliers (Cont.)
Andy Mark

## Slide 9: Suppliers (Cont.)
Laird Plastics

## Slide 10: Suppliers (Cont.)
Stock Drive Product and Sterling Instrument (SDP/SI)

## Slide 11: Suppliers (Cont.)
Metal-By-The-Foot

## Slide 12: Types of Machining
Drilling
Cutting
Bending

## Slide 13: Tools Needed
Marker or drawing utensil
Punches
Ball Peen Hammer
Combination Square
Dial Calipers
Correct Size Drills (sometimes smaller bits)

## Slide 14: How To Drill Precise Hole Locations
Know where your hole is
Measure and mark it
Measure it again
Center Punch
Drill pilot hole if needed
Drill with a full sized bit
Debur the hole

## Slide 15: Drilling Tips and Tricks
Use a punch
Above ¼ in, drill starter hole
Oscillating pressure with hole saws

## Slide 16: Cutting tips and tricks
Start with strips of smallest dimension
Keep leftover strip if still big enough to be useful
Irregular parts, use CAD
On some tools allow space for the blade

## Slide 17: Cutting Tips and tricks (cont.)
Shaft
  Add 1/8th inch to wanted length
  Turn as you cut
  File edge to a chamfer

## Slide 18: Cutting Tips and tricks (cont.)
Extrusion
  Do not add 1/8th
  Hand File sharp edges
  Avoid chamfer

## Slide 19: Bending Tips and Tricks
Draw Bend Line
Compensate for bend radius
Make jig if needed
Over bend for elastic materials

## Slide 20: Bending Tips and Tricks (Cont.)
Other tools you can use
  Vise
  Wood board
  Hammer

## Slide 21: Fasteners
Nuts and Bolts
Screws
Adhesives

## Slide 22: Nuts and Bolts
Nuts
Come in different shapes to suit different purposes
Lock nut
T-nut
Bolts
Come in a multiple sizes and heads

## Slide 23: Screws
Most of the time used with wood
Can be done with metal
Bolt and Screw can be used interchangeably only difference is in application

## Slide 24: Adhesive
Many different types and specs
Tape
Epoxy
Glue